## Slide 1: Building SW Everyone Can Trust
Safety Requirements on SW in Automotive Applications

## Slide 2: Agenda
Why SW is safety-relevant?
Technical understanding of Safety. ASIL
Lifecycle
Coverage
Methods and measures
Independence and decomposition

## Slide 3: Why SW is safety-relevant?

## Slide 4: SW is literally everywhere
“Old” (automotive) functions – SW for performance
  Engine control
  Braking control
  Passive safety
“New” functions – SW is essential
  Active safety
  ADAS
  Autonomous driving

## Slide 5: SW failures are systematic failures
Once made, SW bugs will exist in any number of SW copies
Putting more SW units work in parallel without redundancy does not help
No probabilistic model!
Therefore, process is important!

## Slide 6: SW is new but the automobile is not
Weight: 600 to 75 000 kg
Velocity: up to 60 m/s
People inside: 1 to ~200
People outside: many more
DANGER!

## Slide 7: Technical understanding of Safety. ASIL
Quantifying universal needs

## Slide 8: What is Safety?
Safety – absence of unreasonable risk in the presence of hazards
  Unreasonable risk – risk acceptable from the standpoint of societal moral concepts
    Risk – combination of probability of a harmful event and the severity of harm it causes
  Hazard – potential source of harm

## Slide 9: We have to agree that…
Risk acceptability is independent of most factors:
  Society (country, region, culture, religion…)
  Person (gender, age, beliefs…)
  Situation (victim – pedestrian / driver, reckless / cautionary)
  Harm (leg vs. arm, deafness vs. blindness)
  It doesn’t work like that! However, that’s the current state of the art
  More details: The Moral Machine by MIT Media Lab, “World Values Map” by Engelhard, Cultural Theory of Risk

## Slide 10: Now everything is easy…
Risk
Acceptable risk
SYSTEM 1
System which is safe by default
(risks it bears are acceptable)
SYSTEM 2
Non-safe system
Safety measures
SYSTEM 2
System “made safe”

## Slide 11: Necessary elements of the safety lifecycle
Any safety lifecycle has those elements (automotive, avionics, nuclear, …)
Risk
Risk assessment
SYSTEM 1
SYSTEM 2
Preliminary risk
assessment
Оценка мер безопасности
(«How safe is safe enough?»)
SYSTEM 2
Safety validation

## Slide 12: Different “flavors” of safety
Why there are many “safeties” (electric safety, functional safety, safety of the intended functionality etc.)
  Different hazards require different ways of protection
  Bureaucracy
    Local, national and international legislation
    Industrial regulation
    Traditions

## Slide 13: Different hazards require different safety measures
(focusing on automotive engineering)
Hazards
«From within»
«From outside»
Component failures
Human actions
Environment
Intentional
Unintentional

## Slide 14: Different hazards require different safety measures
(focusing on automotive engineering)
Hazards
«From within»
«From outside»
Component failures
Human actions
Environment
Intentional
Unintentional
Cybersecurity
ISO 21448 “Safety of the Itended Functionality”
Functional safety

## Slide 15: Functional safety
Absence of unreasonable risk related to component malfunction
  Malfunction – system failure or change of system behavior violating the development goals
  There is no formal definition for development goals
  Analysis is required

## Slide 16: We have to agree that…
Following the predefined lifecycle decreases risks (increases safety)
Risk acceptable by social moral concepts can be defined by one standard worldwide
Safety assessment can be reduced to the assessment of safety arguments
  It seems valid. There is nothing refuting those statements.

## Slide 17: ISO 26262 Lifecycle

## Slide 18: ISO 26262 introduces ASILs
Risk
Acceptable Risk
QM
Automotive Safety
Integrity Level (ASIL)
ASIL A
ASIL D
…
System is “a bit unsafe”
“Minimum” safety measures required
Risk associated with system failure exceeds the acceptable level significantly
“Maximum” safety measures required

## Slide 19: ISO 26262 on this picture
Risk
Acceptable level of risk set implicitly by the standard
SYSTEM 1
SYSTEM 2
Hazard analysis for target ASIL determination
System analysis for definition of required safety measures
SYSTEM 2
HW & SW analysis validate
the assumptions made on
system level.

## Slide 20: Lifecycle
Software safety lifecycle per ISO 26262-6

## Slide 21: ISO 26262 Part 6

## Slide 22: SW development lifecycle

## Slide 23: SW development lifecycle
Specification of SW safety requirements
  SW safety requirements are created based on the system-level requirements
    Requirements of different levels are linked by “traces” (UML/SysML <<implement>>) link. Traceability graph is created.
  SW safety requirements (SSR) inherit ASIL from system-level (SysR) requirements
    If two or more SSR implement one SysR, “ASIL decomposition” is applied to reduce the ASIL due to redundancy
  Writing requirements is a separate skill
    Requirement shall be verifiable, atomic, clear, complete and many more
    “Requirement Writing Guide” from INCOSE is a good start

## Slide 24: SW development lifecycle
SW architectural design
  Architecture specifies modules AND behavior
    Block diagram is not architecture
  There are standardized ways to express your architecture
    No, NOT Visio!
  Good architecture will help you
    Easy verification & analysis
    Good safety arguments
    Easy unit specification
    Low risk due to technical debt
  Bad architecture will kill you
    Lack of the above

## Slide 25: SW development lifecycle
Unit design and implementation
  One often hears that “code is the best documentation”
    This is correct at unit level ONLY
  SSRs are assigned to units
  Unit testing is based on SSRs AND best practices
  Compiler checks and other means of automated deployment help at unit level ONLY

## Slide 26: SW development lifecycle
“Right branch” of the V-Model
  Unit testing – SSRs (less) and automated checking (more)
  Architecture verification – checks of dependencies and independencies
  Verification of SSRs – 100% SSR based. Without requirements, no verification.

## Slide 27: Coverage
Test coverage at different levels

## Slide 28: Coverage @ Unit testing
Statement coverage
  Every statement has been invoked at least once
Branch coverage (condition coverage)
  Every point of entry and exit
  Every control statement has been tested for all outcomes
  Every non-constant Boolean has been tried for both TRUE and FALSE

## Slide 29: Coverage @ Unit testing
Modified Conditions/Decisions Coverage (MC/DC)
  Branch coverage, plus the following:
  Every non-constant condition (part of Boolean expressions) has been evaluated for both TRUE and FALSE
  Every non-constant condition has been shown to independently affect the value of the expression

## Slide 30: Coverage @ Unit testing
Selection of coverage model
  QM & ASIL A: statement coverage
  ASIL B & C: branch coverage required, MC/DC recommended
  ASIL D: MC/DC required

## Slide 31: Coverage @ architecture verification
Data transmission pathways within safety-relevant (SR) parts of the architecture
Independence between SR and non-SR parts of the SW

## Slide 32: Coverage @ SW verification
All SSRs has been tested
  Explicitly
  Fully
Writing good test cases is a separate skill.
  Test-cases shall be written independently from developers
  Test-cases shall be written independently from SSR authors

## Slide 33: Target coverage level
100%
on each level

## Slide 34: Methods and Measures

## Slide 35: Methods & Measures tables
16 tables with suitable methods and measures for every lifecycle step
ASIL-dependent
  A & B – mostly the same measures
  C – more complex than B (semiformal verification, higher requirements on testing)
  D – much more complex than C

## Slide 36: Methods & Measures tables
16 tables with suitable methods and measures for every lifecycle step
Designations
  – : not recommended
  o : no information
  + : recommended
  ++ : highly recommended

## Slide 37: Modelling and Coding Guidelines

## Slide 38: Design notations

## Slide 39: SW architecture design

## Slide 40: Error detection at architectural level

## Slide 41: Error handling at the architectural level

## Slide 42: Verification of the SW architectural design

## Slide 43: Notations for SW unit design

## Slide 44: Unit design principles

## Slide 45: Unit-level verification

## Slide 46: Unit testing

## Slide 47: Test cases for unit testing

## Slide 48: Structural coverage metrics

## Slide 49: Integration testing

## Slide 50: Test cases for SW integration testing

## Slide 51: Independence and Freedom from Interference

## Slide 52: What’s the difference?
Independence – complete absence of interplay between A and B
Freedom from Interference – failures do not propagate between A and B
Freedom from interference (FfI) is enough to argue for safety

## Slide 53: “Three pillars” of FfI
Timing
Memory
Exchange of information

## Slide 54: Timing
Failures to look for:
  Blocking of execution
  Deadlocks
  Livelocks
  Incorrect allocation for execution time
  Incorrect synchronization

## Slide 55: Memory
Failures to look for
  Corruption
  Read or write access denied when needed

## Slide 56: Exchange of information
Failures to look for
  repetition of information;
  loss of information;
  delay of information;
  insertion of information;
  masquerade or incorrect addressing of information;
  incorrect sequence of information;
  corruption of information;
  asymmetric information sent from a sender to multiple receivers;
  information from a sender received by only a subset of the receivers;
  blocking access to a communication channel.

## Slide 57: Outlook and Final Thoughts

## Slide 58: Take home message
If you are developing a safety-relevant system, you are not alone
Things to have a look at
  Systems Engineering (book by Kosiakoff is the best entry point)
  Safety Engineering (books by Nancy Leveson and Joseph Miller may be of interest)
Currently System and Safety Engineering is much more a “trade” than an established engineering discipline

## Slide 59: Take home message
Ask [yourself] questions, provide arguments
  “Why do we think that it is OK?”
  Bad arguments
    The boss said so
    It works
    It has always been like this
  “What is the state of the art?”
  “How can we justify it?”
  Bad arguments
    Money
    Time pressure

## Slide 60: Take home message
Think in goals, not tools
Organize your work
  Ensure that you CAN land where you want to land
  Lifecycle is not a process!
Talk to each other
  Safety shall not be an optional feature
  Discussing safety arguments does not violate IP
  Safety is a societal factor

## Slide 61: Do you want to talk about it?
Oleg Kirovskii
Oleg.Kirovskii@gmail.com
Telegram: @nilometrist

## Slide 62: Thank you very much for your attention!
“We decided to do it not because it’s easy, but because it’s hard”
(JFK about going to the Moon)